## Slide 1
INDIA · ENERGY & CHEMICALS · POLICY BRIEF
From fuel to chemicals
India's rupee-vs-dollar import-substitution case
Ethanol frees petrol → the freed naphtha cracks into the very chemicals India imports → a PLI makes that domestic production bankable. Rupee feedstock, displacing dollar imports.
Built on PPAC Ready Reckoner · DGCIS/Tradestat · FADA · Vahan · ICIS · PIB

## Slide 2
THE PROBLEM
Where the dollars go — ~$274 bn of essential imports
$718 bn
total imports (CY2024)
$274 bn
essential imports / yr
$199 bn
energy (crude+coal+gas)
~54%
of India's trade deficit
is mineral fuels
Chart: 
| Crude oil | Electronics | Gold | Chemicals | Coal | LNG+LPG | Edible oil | Fertiliser
US$ bn | 137 | 90 | 60 | 47 | 32 | 30 | 17 | 11
Every essential has a substitution lever —
ethanol/EV for fuel · oilseed mission for edible oil · domestic fertiliser. Chemicals is the only large one with no PLI.
Sources: DGCIS/Tradestat (HS-27, CY2024) · PPAC RR (crude, FY25) · trade reporting.

## Slide 3
LEVER 1
Ethanol frees petrol — and it's paid for in rupees
7.7 → 11.5
MMT petrol freed (E20 → E30)
35 – 53%
of substitutable polymer
imports, if cracked
₹65k–97k cr
rupee cost (domestic —
to farmers, distilleries)
$5 – 9 bn
forex freed (crude/petchem)
₹
Rupee in — stays home
Indian cane / grain feedstock, domestic distilleries, rural labour. ~2.5–3× local multiplier — the cost recirculates as farm income, not a payment that leaves the country.
$
Dollars out — saved
The freed petrol either cuts crude imports, is exported, or is cracked into petchem — each worth $5–9 bn of forex. Premium over fuel value is ~₹14/L — but in rupees, not dollars.
Conversions per PPAC RR Table 9.2/9.3 (petrol 1 MT = 1.411 KL = 8.88 bbl). Same barrels, one lens — not additive.

## Slide 4
THE REFINING SQUEEZE
Margins have normalised — petrochemicals are the next lever
1
GRM $10-12 → $5-6/bbl
Indian refiners' margins fell as the discounted-Russian-crude edge faded.
2
EU ban + sanctions
Products from Russian crude barred from the EU (Jan 2026); flows from 11 refineries fell ~69%.
3
Petchem integration
+$1.5–2/bbl marginal GRM; full crude-to-chemicals earns $60–80/bbl vs $15–25 for fuels.
The takeaway: the fuel margin is thin and geopolitically levered; the durable value is moving down the chain into chemicals.
Sources: Argus/Platts (cracks, GRM) · Vortexa/KSE (EU ban) · Digital Refining (integration economics).

## Slide 5
LEVER 2
The petrochemical import tree — ~$15 bn substitutable
Made from the same petrol-range streams (naphtha → olefins, reformate → aromatics). Each with its 8-digit HSN code.
Styrene monomer
2902 50 00
~100%
Acrylonitrile
2926 10 00
~100%
Polycarbonate (BPA)
3907 40 00
~90-100%
MDI / TDI (isocyanates)
2929 10 20 / 10
~85-90%
PVC resin
3904 10 10
~55-75%
Polyethylene
3901 10/20/40
~25-40%
Polypropylene
3902 10 00
~20-25%
MEG · epoxy · nylon · PTA
2905/3907/3908
high / partial
Import dependence, colour-coded. Ethanol-freed feedstock alone could substitute 35–53% of these. Source: ICIS flowchart · MoC · DGCIS.

## Slide 6
THE GAP
14 PLI sectors, ₹1.97 lakh cr — chemicals is not one of them
14 sectors
under PLI (₹1.97 lakh cr)
$74 bn
India's chemical import bill
~$15 bn
petroleum-linked, substitutable
0
PLI for chemicals
The template already works
The electronics PLI turned India from a mobile-phone importer into a net exporter in ~4 years. The same instrument, pointed at the HSN-coded chemical import list — polycarbonate, MDI/TDI, styrene, acrylonitrile — is the obvious next move. Pharma, autos, solar, steel and textiles are all covered; the 4th-largest essential dollar drain is not.
Sources: PIB (PLI programme) · MoC Statistics-at-a-Glance · DGCIS.

## Slide 7
THE CASE
A Production-Linked Incentive for chemicals
On record: FM Nirmala Sitharaman — the government “will consider a PLI for chemicals & petrochemicals”; the Ministry of Chemicals is formulating one (import-substitution of intermediates).
Target
The HSN-coded, high-dependence list: PVC, PE, PP, styrene, polycarbonate, MDI/TDI, ACN, MEG, epoxy, nylon.
Priority
The ~85-100%-imported cluster first — engineering plastics & polyurethanes (deepest gap, highest value).
Incentive
4–6% on incremental production, tapering as capacity matures; anchored in PCPIRs.
Feedstock link
Tie to crude-to-chemicals crackers and the ethanol-freed petrol pool — rupee feedstock, dollar imports out.
The prize: substituting half the ~$15 bn petroleum-linked chemical imports saves ~$7–8 bn/yr of forex, permanently — a 4-6% incentive costs a fraction of the forex it protects.
Sources: Indian Chemical News / Deccan Herald (FM statement) · PIB (policy redraft) · Invest India.

## Slide 8
THE THROUGH-LINE
One coherent import-substitution stack
1
Ethanol frees petrol-range volume — paid in rupees, to Indian farmers
2
Freed naphtha cracks into the very petrochemicals India imports in dollars
3
A chemicals PLI makes that domestic production bankable — the missing lever
Rupee feedstock displacing dollar imports — energy security, a narrower current-account gap, and rural income, in one policy loop.