## Slide 1
INDIA · 2026 · BUYER'S GUIDE
Fuel & vehicle choices
Petrol · Diesel · CNG · Hybrid · Electric — what each really costs to run
The honest version — with real on-road public EV charging rates (₹18–26/kWh), not just cheap home charging. Metro prices, real-world efficiency, pros and cons.
Prices July 2026 (metro avg) · efficiency SIAM-based · charging tariffs advertised 2026

## Slide 2
THE RUNNING-COST LADDER
What it costs to drive 1 km
Car basis, ₹ per km at the wheel. EV swings hugely with where you charge.
Chart: 
| Petrol (E20) | EV — public fast | Diesel | Hybrid | CNG | EV — home
₹/km | 6.25 | 3.3 | 4.5 | 4.17 | 3.15 | 1.2
The catch
On home charging the EV is unbeatable — ₹1.20/km. But on a real public fast charger it's ₹3.30/km — about the same as CNG, and dearer than you'd expect. CNG is the cheapest fuel you can just pump.
Prices: petrol ₹100/L · diesel ₹90/L · CNG ₹82/kg · home ₹8/kWh · public DC ₹22/kWh. Efficiency real-world (SIAM-based).

## Slide 3
THE NUMBERS
Price, efficiency & cost per km
Fuel
Pump price
Real-world efficiency
Cost / km
Petrol (E20)
₹100 / litre
16 kmpl
₹6.25
Diesel
₹90 / litre
20 kmpl
₹4.50
Hybrid (petrol)
₹100 / litre
24 kmpl
₹4.17
CNG
₹82 / kg
26 km/kg
₹3.15
EV — home charge
₹8 / kWh
6.7 km/kWh
₹1.20
EV — public fast
₹22 / kWh
6.7 km/kWh
₹3.30
Metro July 2026 prices · efficiency real-world (below SIAM certified, incl. E20 mileage drop) · car basis, 15 kWh/100 km EV.

## Slide 4
THE CORRECTION
The EV number depends entirely on where you plug in
HOME CHARGING
₹8/kWh
₹1.20 / km
Overnight, domestic slab. This is the “EV is 5× cheaper” number everyone quotes — but it needs a parking spot with a plug.
PUBLIC DC FAST CHARGING
₹18–26/kWh
₹3.30 / km
Tata Power ₹17 · ChargeZone ₹20–25 · Statiq ₹15–25. On the road the EV costs about the same as CNG — and more than a diesel is often assumed to.
Advertised 2026 tariffs (GreenTax, ChargeZone, network sites). Home charging assumes a dedicated wall-box + domestic connection.

## Slide 5
PROS & CONS
The three you can just refuel
Petrol (E20)
₹6.25/km
✓ Cheapest to buy, widest choice
✓ Available everywhere, smooth
✓ Best resale, no range worry
✗ Highest running cost
✗ E20 trims mileage 2–6%
✗ Most heavily taxed fuel
Diesel
₹4.50/km
✓ Great mileage & torque
✓ Ideal for highways / high-km
✓ Long range per tank
✗ Pricier to buy & service
✗ 10-yr bans in some cities
✗ Higher NOx / upkeep
CNG
₹3.15/km
✓ Cheapest fuel you can pump
✓ Cleaner burn, low running cost
✓ Bi-fuel fallback to petrol
✗ Sparse stations, queues
✗ Cylinder eats boot space
✗ Fewer models, less power
Car basis. CNG has the lowest pump-fuel cost per km of any fossil option; petrol the highest.

## Slide 6
PROS & CONS
The two that change the maths
Strong Hybrid
₹4.17/km
✓ ~40% better mileage than petrol
✓ No plug, no range anxiety
✓ Low emissions, smooth, quiet
✓ Self-charging battery
✗ Higher upfront price
✗ 40% GST on large hybrids
✗ Battery cost over long term
✗ Fewer models on sale
Electric (EV)
₹1.20–3.30/km
✓ Unbeatable on home charging
✓ Zero tailpipe, 5% GST
✓ Very low maintenance, quiet
✓ Cheapest per km — if you charge at home
✗ Public fast charging dear (₹18–26/kWh)
✗ High upfront cost
✗ Range / charging-time anxiety
✗ Battery replacement & resale risk
The EV case lives or dies on home-charging access — the single biggest variable in the whole comparison.

## Slide 7
TOTAL COST OF OWNERSHIP
5 years on a real Tata Nexon — all four fuels
Same model, on-road: petrol ₹12.3L · CNG ₹13.3L · diesel ₹14.5L · EV ₹16.0L. 12,000 km/yr, net of resale.
Chart: 
| Petrol | CNG | EV | Diesel
Depreciation (on-road − resale) | 6.5 | 7.4 | 9.6 | 8
Fuel + maintenance (5 yr) | 4.35 | 2.6 | 1.4 | 3.6
5-yr total · EMI/month
CNG
₹10.0L
₹27.6k
Petrol
₹10.9L
₹25.5k
EV
₹11.0L
₹32.9k
Diesel
₹11.6L
₹30.1k
EMI = on-road, 5-yr, ~9% (EV 8.55% green loan)
The crossover: at 12,000 km/yr, CNG wins and EV ≈ petrol — the EV's higher price offsets its cheap running. Above ~25,000 km/yr with home charging, the EV pulls clearly ahead.
Nexon on-road prices (CarWale/CarDekho, Jul 2026); Grand Vitara hybrid a segment up (~₹19.5L, ₹40.5k EMI). Loan rates SBI/HDFC 2026. EV resale ~40% is the key uncertainty.

## Slide 8
WHAT YOU ACTUALLY PAY
The full stack — upfront, fixed costs & EMI
Tata Nexon, on-road & financed. Beyond fuel, a car costs you an EMI, insurance, road tax and upkeep.
Fuel
On-road
EMI / mo
Insurance / yr
Maint / yr
Fuel / yr
All-in / yr
Petrol
₹12.3L
₹25.5k
₹28k
₹12k
₹75k
₹4.21L
CNG
₹13.3L
₹27.6k
₹29k
₹14k
₹38k
₹4.12L
Diesel
₹14.5L
₹30.1k
₹32k
₹18k
₹54k
₹4.65L
EV (home)
₹16.0L
₹32.9k
₹38k
₹6k
₹14k
₹4.53L
Financed, the EV's cheap fuel doesn't cover its bigger EMI at 12,000 km/yr — CNG is cheapest all-in. EVs pay more insurance, but many states waive road tax (~₹1L off the on-road).
All-in/yr = EMI×12 + insurance + maintenance + fuel (excl. depreciation). EV on public charging ≈ ₹4.79L/yr. Prices/rates 2026.

## Slide 9
THE BOTTOM LINE
Which one is right for you?
1
Home charging + city driving → Electric — nothing beats ₹1.20/km
2
High km / highways, no home plug → Diesel or CNG — cheap to run, quick to fill
3
Want efficiency with zero hassle → Strong hybrid — ~24 kmpl, no charging
4
Low usage, lowest upfront cost → Petrol — cheap to buy, dear to run
The EV wins on running cost only with home charging. On public fast chargers it's a CNG, not a giveaway — plan around where you'll actually plug in.